LOGICAL WAN STRUCTURE

SITE-SPECIFIC BREAKDOWN OF LAN SERVICES

## 🏢 Headquarters (HQ)
### 🔹 Staff LAN
- Purpose: Core user access for internal operations
- Services:
  - DHCP for dynamic IP assignment
  - DNS for internal name resolution
  - Access to internal servers (file, email, database)
  - Internet access via centralized NAT/PAT
  - VLAN segmentation for department-level isolation
### 🔹 Guest LAN
- Purpose: Internet-only access for visitors
- Services:
  - DHCP with restricted scope
  - NAT/PAT for outbound traffic
  - ACLs to block access to internal resources
### 🔹 Server LAN
- Purpose: Hosts centralized services
- Services:
  - Static IPs for servers
  - Web, DNS, Email, and File services
  - Internal routing and service backbone
  - Backup and redundancy systems
### 🔹 Management LAN
- Purpose: Secure administrative access
- Services:
  - SSH/Telnet for device configuration
  - SNMP for monitoring
  - AAA (RADIUS/TACACS+) for authentication
  - Syslog and NTP services
### 🔹 Wireless Control LAN
- Purpose: Wireless infrastructure management
- Services:
  - CAPWAP traffic for WLC and APs
  - Centralized SSID management
  - VLAN tagging for wireless clients
### 🔹 Internet Gateway LAN
- Purpose: External connectivity
- Services:
  - NAT/PAT for all outbound traffic
  - Firewall and IDS/IPS
  - BGP or static routing to ISP
  - DMZ (optional) for public-facing services

## 🏬 Branch A
### 🔹 Staff LAN
- Purpose: Local user access
- Services:
  - DHCP relay to HQ or local DHCP
  - DNS via HQ or local cache
  - Access to HQ-hosted services (via routing)
  - Internet access routed through HQ
### 🔹 Guest LAN
- Purpose: Visitor access
- Services:
  - DHCP with limited scope
  - Internet-only access via HQ NAT/PAT
  - ACLs for isolation
### 🔹 Wireless Control LAN
- Purpose: AP management
- Services:
  - CAPWAP traffic to HQ WLC
  - VLAN tagging for SSIDs
  - Local fallback if autonomous APs are used

## 🏬 Branch B
### 🔹 Staff LAN
- Purpose: Remote user access
- Services:
  - DHCP relay or local DHCP
  - DNS via HQ or local cache
  - Access to internal services via WAN
  - Internet routed through HQ
### 🔹 Guest LAN
- Purpose: Visitor access
- Services:
  - DHCP with restricted scope
  - Internet-only access via HQ
  - ACLs for segmentation
### 🔹 Wireless Control LAN
- Purpose: Wireless infrastructure
- Services:
  - CAPWAP traffic to HQ WLC
  - VLAN tagging for SSIDs
  - Optional autonomous AP support

LAYER 3 TOPOLOGY

# Reliability

- To ensure reliability, all LANs  that make up the WAN have dual routers, with one active router and the other in standby mode.
- Branch A and B forward their internet traffic to the HQ router, which is responsible for consolidating internet traffic and sending it to the internet gateway LAN.

## 🌐 Layer 3 Topology Overview
### 📌 Topology Type: Dual-Hub Centralized WAN
This design employs a redundant dual-hub architecture at the headquarters (HR), ensuring high availability, scalability, and efficient routing across the enterprise WAN.
### 🧭 Topology Description
- Headquarters (HR):
  - Two core routers: HR-R1 and HR-R2
  - Interconnected via a dedicated Layer 3 link for OSPF adjacency and internal failover
  - Each router connects independently to the Internet Edge Router, enabling redundant upstream access
- Branch Sites (A and B):
  - Each branch router has dual WAN links:
    - One to HR-R1
    - One to HR-R2
  - Links are configured as point-to-point /30 subnets
- Routing Protocol:
  - OSPF Area 0 is used across all Layer 3 links
  - Equal-cost multipath (ECMP) routing enables automatic load balancing and failover

## 🔍 Design Rationale – Key Features
### I. Redundancy
- A. Dual core routers at HQ eliminate single points of failure.
- B. Branch routers connect to both HQ routers for WAN path redundancy.
- C. Inter-router link between HR-R1 and HR-R2 ensures internal failover capability.
### II. Scalability
- A. Modular design allows easy addition of new branches or services.
- B. Centralized architecture simplifies expansion and policy enforcement.
### III. Routing Efficiency
- A. OSPF Area 0 used across all Layer 3 links.
- B. Equal-cost multipath (ECMP) routing enables automatic load balancing.
- C. Fast convergence through direct OSPF adjacency between HQ routers.
### IV. Security and Control
- A. Centralized Internet access via edge router allows unified security policies.
- B. Simplified traffic monitoring and firewall placement at the edge.
### V. Operational Resilience
- A. Simulated link failures confirm uninterrupted routing via alternate paths.
- B. Design supports graceful degradation under partial network outages.
### ⚙️ Configuration Highlights
- IP Addressing: All WAN links use /30 subnets for efficient point-to-point routing.
- OSPF Setup:
  - All routers participate in Area 0
  - OSPF automatically balances traffic across equal-cost paths
- Failover Testing: Simulated link failures confirm uninterrupted routing via alternate paths

Logical topology designs for each LAN

Headquarters

Branch A

Branch B

Internet gateway LAN

IP address planning

Branch A

IPv4
- Range: 10.0.10.0/24–10.0.19.0/24

IPv6
FD00::/8 will be used for ULA

LAN SEGMENT	PURPOSE	IPV4 SUBNET	IPV6 SUBNET	DHCP Type
Staff LAN	Internet user access	10.0.10.0/24	FD00:0A:01::/64	DHCPv4 + DHCPv6
Guest LAN	Visitor internet access	10.0.11.0/24	FD00:0A:02::/64	DHCPv4 + DHCPv6
Wireless Control LAN	AP management	10.0.12.0/24	FD00:0A:03::/64	DHCPv4 + DHCPv6
Management LAN (local)	Optional fallback access	10.0.13.0/24	FD00:0A:04::/64	Static + DHCPv6
Inter-router link	Branch A ↔ HQ WAN link	10.0.254.0/30	FD00:0A:FE::/126	Static

Branch B

IPv4 Subnet Blocks: Branch B starts at 10.0.20.0/24, following Branch A’s 10.0.10.0/24 range and ends at 10.0.29/0/24.
IPv6 ULA Scheme: FD00:0B:XX::/64 where 0B denotes Branch B and XX maps to LAN segment.
LAN SEGMENT	PURPOSE	IPV4 SUBNET	IPV6 SUBNET	DHCP TYPE
Staff LAN	Internet user access	10.0.20.0/24	FD00:0B:01::/64	DHCPv4 + DHCPv6
Guest LAN	Visitor internet access	10.0.21.0/24	FD00:0B:02::/64	DHCPv4 + DHCPv6
Wireless Control LAN	AP management	10.0.22.0/24	FD00:0B:03::/64	DHCPv4 + DHCPv6
Management LAN (local)	Optional fallback access	10.0.23.0/24	FD00:0B:04::/64	Static + DHCPv6
Inter-router link	Branch A ↔ HQ WAN link	10.0.254.4/30	FD00:0B:FE::/126	Static

HQ

LAN SEGMENT	PURPOSE	IPV4 SUBNET	IPV6 SUBNET	DHCP TYPE
Staff LAN	Internet user access	10.0.0.0/24	FD00:00:01::/64	DHCPv4 + DHCPv6
Guest LAN	Visitor internet access	10.0.1.0/24	FD00:00:02::/64	DHCPv4 + DHCPv6
Server LAN	AP management	10.0.2.0/24	FD00:00:03::/64	Static + DHCPv6
Management LAN	Admin access	10.0.3.0/24	FD00:00:04::/64	Static + DHCPv6
Wireless Control LAN	WLC & AP management	10.0.4.0/24	FD00:00:05::/64	DHCPv4 + DHCPv6

Internet gateway LAN

Subnet	Purpose	Notes
FD00:00:FE::/64	Internet Gateway Core	NAT64, firewall, BGP/static routing
FD00:00:FD::/64	DMZ Services	Public-facing IPv6 services
FD00:00:FF::/126	ISP Link	Point-to-point IPv6 uplink

IPv6 Highlights
- FE = Internet Gateway Core
- FD = DMZ
- FF = ISP link
- Use SLAAC + DHCPv6 for DMZ clients if needed
- Enable RA + DNS64/NAT64 for IPv6-only clients accessing IPv4 services

Device	IPv4	IPv6	Notes
Internet Gateway Firewall 1	10.0.0.241	FD00:00:FE::1	Primary outbound NAT, DMZ filtering
Internet Gateway Firewall 2	10.0.0.242	FD00:00:FF::1	Redundant failover unit
HQ Core Router (to Gateway)	10.0.0.243	FD00:00:FE::3	Internal uplink to Gateway LAN
ISP Router	10.0.0.221	FD00:00:FF::1	External uplink

Next step is vlan planning, the ip planning will be modified here and there